## Slide 1
Computer Networks (CN) CTMTCSE SIV P2
Syllabus and Establishment of this Subject
Dr. Vijeta Khare

## Slide 2: Syllabus and Books

## Slide 3
Teaching Scheme |  |  |  |  | Evaluation Scheme |  |  |  |  |  |  |  | 
Th | Tu | Pr | C | TCH | Theory |  |  |  |  |  | Practical |  | Tot al
 |  |  |  |  | Internal Exams |  |  |  | University Exams |  | University Exams (LPW) |  | 
 |  |  |  |  | TA-1/TA-2 |  | MSE |  | Marks | Hrs. | Marks | Hrs. | 
 |  |  |  |  | Marks | Hrs. | Marks | Hrs. |  |  |  |  | 
03 | 00 | 00 | 03 | 03 | 25 | 00:45 | 50 | 01:30 | 100 | 03:00 | - | - | 200
CTMTCSE SIV P2: Computer Networks
Objectives
To learn about data communication
To learn about the network devices and its functionality.
To learn the services running on various network layers.
To learn the network topologies and their implementation.
To understand routing protocols.

## Slide 4
UNIT – I
Data Communication
Data and Signals: Analog and Digital, Periodic Analog Signals, Digital Signals, performance, Digital Transmission: Digital to Digital and Analog to Digital Conversion, Transmission Modes, Analog Transmission. Bandwidth Utilization: Multiplexing, Spread Spectrum.
UNIT – II
History and Models
Introduction, history and development of computer networks and internet, various protocols and standards, network topologies, Network Categories: LAN, MAN, WAN, network reference model OSI and TCP/IP protocol suite.
UNIT – III
Physical and Link
Various transmission media (guided media and unguided media), wireless transmission media, errors in transmission: attenuation, noise. Repeaters. Data Link Layer: Error Detection & Correction Techniques, Elementary Data Link Layer Protocols: Simplex, Stop and Wait, Sliding Window Protocol.
UNIT – IV
Middle Layer
Medium Access Control sublayer: channel allocation problem, Multiple Access Protocols: ALOHA, CSMA, CSMA/CA, CSMA/CD, Ethernet, Data link layer switching, VLANs. Networking Devices (hub, switch, bridge, router, gateway, repeater), comparison of network devices, network core (packet switching, circuit switching).
UNIT – V
Network Layer
Types of Addressing, IPv4 and IPv6 Addressing scheme, Transition from IPv4 to IPv6, IP forwarding, classful and classless addressing (subnet, supernet), NAT, Basics of routing algorithms.

## Slide 5
Reference Books
Computer Network by Andrew S. Tanenbaum and David J. Wetherall, 5th Edition
Computer Networking- A Top-Down approach (7th edition), Kurose and Ross, Pearson
Computer Networks- A Top-Down approach, Behrouz Forouzan, McGraw Hill
TCP/IP Protocol Suite (4th edition), Behrouz Forouzan, McGraw Hill
Data Communications and Networking By Behrouz A. Forouzan, 5th Edition

## Slide 6: Assignment’s and practical’s
Are to be done yourself
  You may discuss the assignments with other students
  You may help (and get help with) debugging
  You may not give your source code to anyone

## Slide 7: Why you should study this course?
Because of Learning:
How data travel between computers
You will learn various networking technologies
Various protocol learning
Because of Importance of the subject:
Placement in few companies
Competitive Exams (7% of exam is covered from this subject)

## Slide 8: Course Outcome
Understand the architecture of various networking technologies
Analyze the requirements of the organization and able to select the appropriate topology and structure of networks.
Have operational knowledge of managing the networks of organization.
Design the network for organization with better network efficiency parameters

## Slide 9: Pre requisites for this course
Knowledge of a programming language: C or C++ and basic platform knowledge of Linux
You should be able to convert high level descriptive algorithm into a working program using C/C++ programming language
Knowledge of basic mathematics, such as: Basic Discrete mathematics

## Slide 10
Unit 1

## Slide 11: What is Computer Network?
Computer Network is a system in which multiple computers are connected to each other to share information and resources.
Wireless
Wired
Network
Devices
Computers

## Slide 12: Advantages of Computer Network
Better Communication
File Sharing
Entertainment
Flexible Access

## Slide 13: Advantages of Computer Network
Inexpensive System
Instant and Multiple Access
Internet Access
Resource Sharing

## Slide 14: Applications of Computer Network
& Many More….
Business & Finance
Email Services
File & Directory Services
Teleconferencing

## Slide 15: Five Components of Data Communication

## Slide 16: Five Components of Data Communication
Message:
  text, number, images, audio, and video
Sender and Receiver
  devices that send/receive data message
  Computer, workstation, telephone, TV, etc.
Transmission medium
  Physical path thru which the message travels
Protocol
  Set of rules governing data communications

## Slide 17: Data flow (simplex, half-duplex, and full-duplex)

## Slide 18: Types of Computer Network
Computer networks can be categories by their size as well as their purpose.
The size of a network can be expressed by the geographic area.
Some of the different networks based on size are:
    Local Area Network - LAN
    Metropolitan Area Network - MAN
    Wide Area Network - WAN

## Slide 19: Local Area Network
A local area network (LAN) is a computer network that interconnects computers within a limited area such as a residence, school, laboratory, university campus or office building.

## Slide 20: Metropolitan Area Network
A metropolitan area network (MAN) is a computer network that interconnects with computer in a metropolitan area like city.
MAN is a larger than LAN but smaller than the area covered by a WAN.
It is also used to interconnection of several local area network.
Navagam
Shapar
Morbi
Rajkot

## Slide 21: Wide Area Network
A wide area network (WAN) is a computer network that exists over a large-scale geographical area.
A WAN connects different networks, including local area networks (LAN) and metropolitan area networks (MAN).
It may be located with in a state or a country or it may be interconnected around the world.
Asia
Africa
America

## Slide 22: Types of Computer Networks - Summary

## Slide 23: Types of Computer Networks - Summary
Basis Of Comparison | LAN | MAN | WAN
Full Name | Local Area Network | Metropolitan Area Network | Wide Area Network
Meaning | A network that connects a group of computers in a small geographical area | It covers relatively large region such as cities, towns | It spans large locality & connects countries together. e.g. Internet
Ownership of Network | Private | Private or Public | Private or Public (VPN)
Design and Maintenance | Easy | Difficult | Difficult
Propagation Delay | Short | Moderate | Long
Speed | High | Moderate | Low
Equipment Used | NIC, Switch, Hub | Modem, Router | Microwave, Radio Transmitter & Receiver
Range(Approximately) | 1 to 10 km | 10 to 100 km | Beyond 100 km
Used for | College, School, Hospital | Small towns, City | State, Country, Continent

## Slide 24: What is Internet?
The internet is a type of world-wide computer network.
The internet is the collection of infinite numbers of connected computers that are spread across the world.
Mobile Network
Global ISP
Regional ISP
Home
Network
Institutional
Network
router
Wired link
wireless
links
smartphone
PC
server
wireless
laptop
Network Components

## Slide 25
Hierarchical organization of the Internet

## Slide 26: Intranet vs. Internet
Intranet
  A private network that is contained within an enterprise
  Could be LANs and WANs
Internet
  A public network of networks
Both are using TCP/IP

## Slide 27: Network edge

## Slide 28: The Network Edge
Computers and other devices are connected at the edge (end) of the network.
These computers are known as hosts or end systems. Router is known as edge router.
mobile network
Global ISP
Regional ISP
Home
Network
Institutional
Network

## Slide 29: Peer to Peer Network
Computers are connected together so that users can share resources and information.
There is no central server for authenticating users, each of them works as both client and server.
e.g. Bit Torrent

## Slide 30: Client – Server Network
Client: Request servers for a task.
  Generally called desktop PCs or workstations.
Server: Receive requests from the clients. Process and response them.
  e.g. Web Server, Email Server

## Slide 31: Network core

## Slide 32: The Network Core: Transmission Techniques
Defines the connection of different network segments together and process to transmit data across the network.
It is implemented through the use of switching techniques.
Switched
Networks
Packet-Switched
Networks
Circuit-Switched
Networks
Message-Switched
Networks

## Slide 33: Circuit Switched Network
A dedicated channel has to be established before the call is made between users.
The channel is reserved between the users till the connection is active.
For half duplex(one way) communication, one channel is allocated and for full duplex(two way) communication, two channels are allocated.
It is mainly used for voice communication requiring real time services without delay.

## Slide 34: Circuit Switched Network – Cont…
Communication via circuit switching involves three phases:
Circuit Establishment
Data Transfer
Circuit Disconnect

## Slide 35
Advantages:
After path is established, data communication without delay.
Very suitable for continuous traffic.
It establishes a dedicated path.
No overhead after call setup.
it is transparent and data passes in order.
Disadvantages:
Provide initial delay for setting up the call.
Inefficient for heavy traffic.
Data rate should be same because of fixed bandwidth.
When load increases, some calls may be blocked.
In data communication, traffic between terminal and server are not continuous. Sometimes more data may come or sometimes there is no data at all. Circuit switching is not efficient because of its fixed bandwidth.

## Slide 36: Message Switching
In this switching method, a different strategy is used, where instead of establishing a dedicated physical line between the sender and the receiver, the message is sent to the nearest directly connected switching node.
This node stores the message, checks for errors, selects the best available route and forwards the message to the next intermediate
The line becomes free again for other messages, while the process is being continued in some other nodes.
Due to the mode of action, this method is also known as store-and-forward technology where the message hops from node to node to its final destination.
Each node stores the full message, checks for errors and forwards it.

## Slide 37
Basic idea:
Each network node receives and stores the message
Determines the next leg of the route, and
Queues the message to go out on that link.
Advantages:
Line efficiency is greater (sharing of links).
Data rate conversion is possible.
Even under heavy traffic, messages are accepted, possibly with a greater delay in delivery.
Message priorities can be used, to satisfy the requirements, if any.
Disadvantages: Message of large size monopolizes the link and storage

## Slide 38: Packet Switched Network
It is not required to establish the connection initially.
The connection/channel is available to use by users. But when traffic or number of users increases then it will lead to congestion in the network.
Packet switched networks are mainly used for data and voice applications requiring non-real time scenarios.

## Slide 39: Packet Switching
The basic approach is not much different from message switching. It is also based on the same ‘store-and-forward’ approach.
However, to overcome the limitations of message switching, messages are divided into subsets of equal length called packets.
This approach was developed for long-distance data communication (1970) and it has evolved over time.
In packet switching approach, data are transmitted in short packets (few Kbytes).
A long message is broken up into a series of packets as shown in Fig. Every packet contains some control information in its header, which is required for routing and other purposes.

## Slide 40
Advantages:
Call setup phase is avoided (for transmission of a few packets, datagram will be faster).
Because it is more primitive, it is more flexible.
Congestion/failed link can be avoided (more reliable).
Problems:
Packets may be delivered out of order.
If a node crashes momentarily, all of its queued packets are lost.

## Slide 41: Switching Network

## Slide 42: Delay, Loss & Throughput
Delay
  As a packet travels from one node (host or router) to the subsequent node (host or router) along this path, the packet suffers from several types of delays at each node along the path.
  Where
dnodal = dproc + dqueue + dtran + dprop
dnodal | = | Total Delay
dproc | = | Processing Delay
dqueue | = | Queuing Delay
dtran | = | Transmission Delay
dprop | = | Propagation Delay

## Slide 43: Delay – Cont…
Processing Delay (dproc)
  The time required to examine the packets header and determine where to direct the packet.
  To check bit level error
  Determine output link
  Delay in terms of microseconds

## Slide 44: Delay – Cont…
Queuing Delay (dqueue)
  A time to wait at output link for transmission.
  Depends on congestion level of router.
  If queue is empty then delay will be zero.
  If queue is full (heavy traffic) then delay will be long.
  Delay in terms of micro second to millisecond.

## Slide 45: Delay – Cont…
Transmission Delay (dtran = L/R)
  An amount of time required for the router to transmit the packet.
  Its depends on packet length(L) and transmission rate(R) of link.

## Slide 46: Delay – Cont…
Propagation Delay (dprop= d/s)
  A time required to propagate from the beginning of the link to router B.
  Depends on the length of physical medium(d) link and propagation speed(s) of link
  Delay in terms of millisecond.

## Slide 47: Packet Loss
Packet loss is the failure of one or more transmitted packets to arrive at their destination.
The loss of data packets depends on the switch queue/buffer. The loss of data packets increases with the increases in the traffic intensity.
It affects the performance
  of the network.

## Slide 48: Throughput
Throughput or Network Throughput is the rate of successful message delivery over a communication channel.
Throughput is measured in bits(data) per second (bit/s or bps)
server, with
file of F bits
send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
Client

## Slide 49: Network Topologies

## Slide 50: Network Topologies
Network topology is the arrangement of the various components(links, nodes, etc.) of a computer network.
Types of network topologies :
  Bus
  Ring
  Star
  Mesh
  Tree
  Hybrid

## Slide 51: Bus Topology
Every computer and network device is connected to single cable
It transmits data only in one direction
Cost effective
Used in small networks
Easy to expand joining two cables together
It is used in early LAN connection

## Slide 52: Bus Topology
Early Ethernet
Notes: ​ Bus topology is a network type in which every computer and network device is connected to single cable.
It transmits the data from one end to another in single direction. No bi-directional feature is in bus topology.

## Slide 53
Advantages:
If N devices are connected to each other in bus topology, then the number of cables required to connect them is 1 ​which is known as backbone cable and N drop lines are required.
Cost of the cable is less as compared to other topology, but it is used to built small networks.
Disadvantages:
If the common cable fails, then the whole system will crash down.
If the network traffic is heavy, it increases collisions in the network.

## Slide 54: Ring Topology
It forms a ring as each computer is connected to another computer, with the last one connected to the first.
Transmission is unidirectional & sequential way that is bit by bit.
Transmitting network is not affected by high traffic or by adding more nodes, as only the nodes having tokens can transmit data.
Cheap to install and expand.

## Slide 55
Advantages:
The possibility of collision is minimum in this type of topology.
Cheap to install and expand.
Disadvantages:
Troubleshooting is difficult in this topology.
Addition of stations in between or removal of stations can disturb the whole topology.

## Slide 56: Star Topology
Computers are connected to a single central hub through a cable.
Fast performance with few nodes and low network traffic.
Easy to troubleshoot & Easy to setup and modify.
Only that node is affected which has failed rest of the nodes can work smoothly.
Hub can be upgraded easily.

## Slide 57
Advantages:
If N devices are connected to each other in star topology, then the number of cables required to connect them is N. So, it is easy to set up.
Each device require only 1 port i.e. to connect to the hub.
Disadvantages:
If the concentrator (hub) on which the whole topology relies fails, the whole system will crash down.
Cost of installation is high.
Performance is based on the single concentrator i.e. hub.

## Slide 58: Mesh Topology
Point-to-point connection to other devices or fully connected.
Traffic is carried only between two connected devices.
Robust, costly but not flexible.
Fault is diagnosed easily.
More cable resource used in setup.

## Slide 59
Advantages:
It is robust.
Fault is diagnosed easily. Data is reliable because data is transferred among the devices through dedicated channels or links.
Provides security and privacy.
Disadvantages:
Installation and configuration is difficult.
Cost of cables are high as bulk wiring is required, hence suitable for less number of devices.
Cost of maintenance is high.

## Slide 60: Tree Topology
It has a root node and all other nodes are connected to it forming a hierarchy.
Also called hierarchical topology.
Mostly used in Wide Area Network – WAN.
Expansion of nodes is possible and easy.
Easily managed and maintained.

## Slide 61: Hybrid Topology
A network structure whose design contains more than one topology is said to be hybrid topology.
It is a combination of two or more topologies.
Flexible & reliable as error detection and easy to troubleshoot.
Scalable as size can be increased easily.

## Slide 62: Comparison of Topologies
 | Bus | Ring | Star | Mesh | Tree
Means | every computer and network device is connected to single cable. | Each computer is connected to another, with the last one connected to the first. | All the computers are connected to a single hub through a cable. | All the network nodes are connected to each other. | It has a root node and all other nodes are connected to it forming a hierarchy.
Cost | Average | Cheap | High | High | High
Used in | Small Network | Expand Network | Small Network | Expand Network | Expand Network
Troubleshoot | Easy, But Cables fail then whole network fails. | Difficult; Failure of one computer disturbs the whole network. | Easy; If the hub fails then the whole network is down. | Easy; Installation and configuration is difficult. | Easy; Central root hub fails, network fails.

## Slide 63: What is Protocol?
Human Protocol(Language)
  “what’s the time?”
  “I have a question”
  Introduction Talk
Network Protocol
  Set of rules
  machines rather than humans
  all communication activity in Internet governed by protocols.
  Protocol is define format, order of message sent and received among network entities, and actions taken on message transmission and reception

## Slide 64: Protocol Layers

## Slide 65: Protocols Layers
To deals with connecting systems that are open for communication with other systems.
OSI Layer Model (Open Systems Interconnection)
Developed by the International Standards Organization (ISO) with seven different layers.
    Physical Layer
    Data Link Layer
    Network Layer
    Transport Layer
    Session Layer
    Presentation Layer
    Application Layer

## Slide 66: Example – Air Plane Travel
ticket (purchase)
baggage (check)
gates (load)
runway takeoff
airplane routing
ticket (complain)
baggage (claim)
gates (unload)
runway landing
airplane routing
airplane routing
Departure
Arrival

## Slide 67: How OSI Layer Works?

## Slide 68: OSI Reference Model: 7 Layers
OSI Model

## Slide 69: Exchange using OSI Model

## Slide 70: Physical Layer
The physical layer is responsible for movements of individual bits from one hop (node) to the next.

## Slide 71: Physical Layer – Cont…
Carries the bit stream over a physical media.
Physical Layer is concerned with:
  Interface and Medium like guided cables
  Representation of bits
  Data rate
  Synchronization of bits
  Line configuration
  Physical topology
  Transmission mode
  Provides physical interface for transmission of information.
  Defines rules by which bits are passed from one system to another on a physical communication medium.
  Covers all - mechanical, electrical, functional and procedural - aspects for physical communication.
  Such characteristics as voltage levels, timing of voltage changes, physical data rates, maximum transmission distances, physical connectors, and other similar attributes are defined by physical layer specifications.

## Slide 72: Bit rate and baud rate
The data rate defines the number of data elements (bits) sent in Is. The unit is bits per second (bps).
The signal rate is the number of signal elements sent in Is. The unit is the baud. There are several common terminologies used in the literature. The data rate is sometimes called the bit rate; the signal rate is sometimes called the pulse rate, the modulation rate, or the baud rate.

## Slide 74: Data Link Layer
The data link layer is responsible for moving frames from one hop to the next.

## Slide 75: Data Link Layer – Cont…
Data link layer is concerned with:
  Framing – divide bits stream into data unit (frame)
  Physical addressing
  Flow control – avoid over overwhelming
  Error control – bit loses, retransmission
  Access control
  Data link layer attempts to provide reliable communication over the physical layer interface.
  Breaks the outgoing data into frames and reassemble the received frames.
  Create and detect frame boundaries.
  Handle errors by implementing an acknowledgement and retransmission scheme.
  Implement flow control.
  Supports points-to-point as well as broadcast communication.
  Supports simplex, half-duplex or full-duplex communication.

## Slide 76: Network Layer
The network layer is responsible for the delivery of individual packets from the source host to the destination host.

## Slide 77: Network Layer – Cont…
In this layer, packet is combined with header and data.
In case of data link layer, packet delivers on the same network.
If two different networks are connected then packet is concern with network layer.
Network layer is concerned with:
  Logical addressing e.g. 192.168.1.1 (IP Address)
  Routing

## Slide 78: Transport Layer
The transport layer is responsible for the delivery of a message from one process to another.

## Slide 79: Transport Layer – Cont…
This layer ensures that the whole message arrives intact and in order.
Transport layer is concerned with:
  Service-point addressing (port address)
  Segmentation and reassembly
  Connection control
  Flow and error control

## Slide 80: Session Layer
The session layer is responsible for dialog control and synchronization.

## Slide 81: Session Layer – Cont…
This layer is network dialog controller – establishes, maintains, synchronizes the interaction among computers.
Session layer is concerned with:
  Dialog control
  Synchronization

## Slide 82: Presentation Layer
The presentation layer is responsible for translation, compression, and encryption.

## Slide 83: Presentation Layer – Cont…
This layer is concerned with the syntax which refers to order in which data is presented and semantics helps in interpreting a particular pattern.
Presentation layer is responsible for:
  Translation
  Encryption
  Compression

## Slide 84: Application Layer
The application layer is responsible for providing services to the user.

## Slide 85: Application Layer – Cont…
This layer provides various services like:
  Network virtual terminal
  File transfer, access and management
  Mail services
  Directory services

## Slide 86: Summary – OSI Layer
Application
Presentation
Session
Transport
Network
Data link
Physical
To allow access to network resource
To translate, encrypt and compress data
To provide reliable process-to-process message delivery and error recovery
To establish, manage and terminate sessions
To move packets from source to destination; To provide internetworking
To transmit bits over a medium; To provide mechanical & electrical specification
To organize bits into frames; To provide hop-to-hop delivery

## Slide 87: TCP/IP Reference Model (Transmission Control Protocol/Internet Protocol)
It was originally defined as having five layers:
TCP/IP is a set of protocols developed to allow cooperating computers to share resources across the network.
  Application Layer
  Transport Layer
  Network Layer
  Data Link Layer
  Physical Network

## Slide 88: TCP/IP Model Architecture

## Slide 89: Difference
OSI (Open System Interconnection) | TCP/IP (Transmission Control Protocol/ Internet Protocol)
OSI provides layer functioning and also defines functions of all the layers | TCP/IP model is more based on protocols and protocols are not flexible with other layers
In OSI model the transport layer guarantees the delivery of packets | In TCP/IP model the transport layer does not guarantees delivery of packets
Follows horizontal approach | Follows vertical approach
OSI model has a separate presentation layer | TCP/IP doesn’t have a separate presentation layer
OSI is a general model | TCP/IP model cannot be used in any other application
It has 7 layers | It has 5 layers

## Slide 90: Difference - Cont…
OSI (Open System Interconnection) | TCP/IP (Transmission Control Protocol/ Internet Protocol)
Network layer of OSI model provide both connection oriented and connectionless service | The Network layer in TCP/IP model provides connectionless service
OSI model has a problem of fitting the protocols in the model | TCP/IP model does not fit any protocol
Protocols are hidden in OSI model and are easily replaced as the technology changes | In TCP/IP, replacing protocol is not easy
OSI model defines services, interfaces and protocols very clearly and makes clear distinction between them | In TCP/IP, it is not clearly separated its services, interfaces and protocols

## Slide 91: Protocol Layers: Summary

## Slide 92
Thank You